## Slide 1: Some tips for digitizing 一些打带的处理及注意事项
That is Joe’ experience on digitizing
以下是本人长年来积累的一些经验

## Slide 2
如发现车某些面料或在他他米面上再车其他的内容，而边缘起狗牙的话，可以在边缘往里0.8 mm的地方走一圈针步长点的三次绣平针。
To have a long length stitch inside of the edge about 0.8mm can avoid the teeth mark around Tatami or extra stitch pattern on the Tatami.
如果他他米的面上还经车其他的内容，可以在他他米打底时在底再沿面上对象的边缘来回走两次行线，针步长一般在3mm以上，这样面上的内容看起来会比较饱满且可以减少狗牙现象。
If there are some other drawing needs be stitched on the Tatami .
Having double running stitching on the underlay of the Tatami
can make the emblem looks better and avoid teeth mark.
打他他米时一定要先沿周围走行线再车下缝，大面积的他他米要在打底时先走两次行线固定。
Have running stitch around edge must be before Tatami stitch,
Double running stitch for registration is needed if it is a large area of Tatami

## Slide 15
shrinkage details

## Slide 16
stitch picture

## Slide 17
the angle of stitch

## Slide 18
the order of stitch

## Slide 19
底线
在打小字母或转弯比较急的花样时，注意底线不能走得太边缘，否则会露底线。1.2mm宽以下的挨针尽量不打底线，只是在起针是下起针使其能拉上底线。Underlay should be stitched inside of the edge as stitching small letters or sharp corners,
Othwise, the bobbin thread will be pull through.
It is unnecessary to have underlay for the satin stitch which length stitch is under 1.2mm and only need to make sure the start stitch can pull the bobbin thread.
underlay

## Slide 20
1 All the badges must be horizontal,symmetrical and the same height strickly on the radian .
2 irrgular badge must be corrected.
3 The length beyond 13 CM of the badge must be stitched in the middle to both side;
4 the rule of punching is to stitch in the middle to the round
5 decrease switching color and cutting possibly. let some stitches go through possibly if needed.
All badges less than 10cm must be stitched through the center and go around the edge of the badge to fix the fabric. all badges more than 10cm must be stitched through the center and go around the edge of the badge with 2.5mm width zigzag and density 3mm

## Slide 21
Normally run one underlay for the letters
run the stitch as this for severe fabric shrinkage
meeting the satin stitch is to come back on stitch at the last stitch .
Run underlay like this for the a little bigger letter or wide satin stitch
meeting wide satin stitch is to come back one long stitch and go across one 0.6mm short stitch then come back one 0.5mm short stitch
stitch as the pictures above for sharp corner, do not use less than 0.8mm short stitch possibly
The stitch must meet in the small badge for two badges(one is big ,the other is small)

## Slide 22
please make the assitant lines for letter badge or the badge is not nomal
The distance between the across assitant line to straight assistant line is 0.2MM
Do not run underlay for satin stitch width about 1mm.
stitch slantly for the satin stitch width less than 1mm to avoid the short stitch less than 0.8mm
The space distance of small letters must be at least 0.5mm to see them clearly.
Letters more than 3.3mm should be stitched by satin stitch,or by running stitch.(unless customer requires)

## Slide 23
stitch fill stitch by golden and silver thread, the running stitch must be 3mm or above if the badge length is less than 10cm;running stitch must be 3.5mm or above if the badge length is more than 10cm.

## Slide 24
Stittch straightly or horizontally for solid stitch when needing fill stitch around the edge.
Do not stitch around the circle,or the badge will be out of shape aftr washing and the density of top stitch and underlay can not be too thick

## Slide 26
applique standard
standard of satin stitch covering placement stitch
picture sample
standard requirement
placement stitch must be 0.75mmf inside from satin stitch,placement stitch should be 2.5mm long.
stardard picture sample
standard of satin stitch covering placement stitch
80% of satin stitch shoud be run inside of the placement stitch,20% run outside of the placement stitch