## Slide 1: 引起走位原因 Causes of poor registration
导致车花走位的原因是多样的，大致可以分为以下几大类：
There were various reasons for leading to poor registration and they are divided by :
1，面料（包括面料的种类以及夹布方式）
Fabric ( including types of material and the method for hooking fabric )
2，机器（一般是框架/针杆箱/针位等）
Machine ( normally refer to frame and needle bar box / needle position )
3，打版（密度/顺序/针法等）
Digitizing ( density / sequence / type of stitch )
4，底面线（底面线调得太紧也会引起走位）
Thread ( too tight for the underlay thread and face thread
will also cause poor registration

## Slide 2: 各原因的因素细分 sub-elements for each cause of the poor registration
面料引起走位的因素:fabric
1，面料太薄 fabric is too thin
2，有弹性的面料 stretchy fabric
3，有绒毛的面料 fluey fabric
4，夹在绷架上太紧或太松
hoop the fabric on the frame too tight or too loose
机器引起走位的因素：Machine
1，机器老化精密度下降
Machine is too old to make the poor precision
2，车花的速度太快
Quick stitching speed
3，零部件干涸，没有注意加润滑油
Parts are not maintained with lubricating oil.
3，针杆变形磨损
Distortion and attrition of the needle bar
4，针位不正确 incorrect position of the needle
5，框架松驰，或皮带老化，轴承磨损 loose of the frame, the aging belt and attrition of the bearing.
打版引起走位的因素：Digitizing
1，打版过程中，打底的线太靠近图形的边缘 underlay thread is too near to the border of the design during digitizing.
2，由于打底的线太稀或角度不对，未能很好固定布料
Fabric can not be fixed properly due to the underlay thread is too thin and the angle is not correct.
3，打版时没有从中心向外围打，造成布料向内收缩也会引起走位 Digitizing does not start from the center of the emblem to the outside and cause the fabric shrunk.
4，底面线的密度太密，以及大面积的车花
The density of the face thread and underlay thread is too high, the stitching area is too big.
5，针法，车花顺序不正确，转色、剪线等频繁 The type of stitch and sequence of stitch is incorrect,
and too much color change and thread cut.

## Slide 3: 短针步的删除 Deletion of the short stitch
通常,若刺繡效果良好,並沒有必要介意花樣數據中的微小針跡。 但有時這些微小針跡會造成斷線降低生產效率,同時也會影響到刺繡效果。 為避免上述問題,在打版時要將花樣整體的最小針跡設定在0.5mm以上,以避免產生微小針跡。 除特殊情況之外,即使將花樣整體的最小針跡設定在0.5mm以上,也不會影響到刺繡效果。
Normally, the embroidery effect looks good and unnecessary to care about the data of the short stitch.
But sometime the short stitch will cause thread to break, reduce the efficiency of the productivity and affect the embroidery effect. In order to avoid the above issue, it is better to set the length of the short stitch above 0.5mm
另外,利用刺繡機的刪除微小針跡功能也可將微小針跡清除。
The short stitch can be delete by the embroidery machine automatically.
將存儲中的花樣數據中的短針跡消除,短針跡的數據將被吸收入其前後的針跡數據中。
Delete the tiny stitch from the embroidery file
and the data of the tiny stitch will be absorbed into the near to stitches.
花樣數據中的短針是造成斷線,漏針,剪線失誤等問題的原因。
Short stitch is the main reason for causing thread to break and missing stitch and incorrect thread cut.
刪除短針不僅可以減少針數,還可以減少由於發生這些問題所造成的停機時間,從而大幅度提高生產效率。
Delete the short stitch not only can reduce the stitch but also can reduce the times of machine stop,
And improve product efficiency.
使用11號繡花針的情況下,通常刪除0.5mm以下的短針跡。
Normally delete the short stitch with length -0.5mm if the needle is #11

## Slide 4
绣花时间基本上完全取决于绣花机的速度，但我们亦可参考一些数据和方法，以减少花样的针数及缩短车花时间。
Time set for stitching depends on the speed of the embroidery machine. In order to reduce stitch account and shorten the time for stitch, we can have the following data and method for reference.
他他米的针距 spacing for filling stitch
他他米适用于一些较大的剌绣范围，一般惯性针距参数设定为 4mm。但由于他他米内的针迹频密，针数远比其它针法为高。我们可以尝试把它的改成 4.5mm 或 5mm这样针数会有一定的减少，而成品亦分别不大。
Filling stitch is applied to the embroidery with big size of stitching, normally, the spacing is set 4mm ,
We can try to set the spacing 4.5mm or 5mm since the filling stitch is very thick,
thus it will not affect the finishing embroidery quality.
尺寸： 10cm X 10cm Dimension : 10cm X 10cm
针距长度 stitch length | 针数 stitch account | 车花时间750 转 750rpm
4.0mm | 13169 | 17分34秒
4.5mm | 11668 | 15分34秒
5mm | 10668 | 14分13秒
剪线或转色 thread cut or color change
自从绣花机懂得自动剪线及可以刺绣多种颜色开始，不但带给我们无限的方便，还给予我们创作灵感。但当每次剪线时，绣花机都会用约0.5秒时间将速度由每分钟700-750转停止，又用0.5秒的时间去剪线，再用约1秒时间将转速升至最高；转色除了要花费剪线的时间外，更要花上约2秒的机头移动时间。 由此可见，在打版的时候应尽量安排颜色相同的针迹同时刺绣，再用单针把不同位置的针迹连接起来，以减少换色及剪线的次数。The embroidery machine brings us a lot of conveniences
since it can cut thread automatically. The machine stops for 0.5 second per each time of thread cut based on 750rpm and another 0.5 second for thread cut and another about 1 second for starting to rise the rotation to 750.
Color change requests extra time and the moving of the machine head also need about 2 seconds.
Thus , try to arrange the object with similar color to stitch simultaneously, and then connect the stitches of different objects by running stitch to avoid the frequencies of color change and thread cut.
他他米的针数 filling stitch account | 剪线次数 times of thread cut | 换色次数 times of color change | 车花时间﹝750转﹞stitch time ( 750rpm)
3507 | 1 | 0 | 约 4 分 43 秒
3772 | 7 | 6 | 约 5 分 33 秒