## Slide 1
用一次性水杯在杯底烫一个小孔，注意孔的边沿不要有毛刺及不顺滑现象。然后将金银线穿过小孔，将杯子倒扣在线上。注意线如果太满，就需要选择稍大的水杯。
Burn a small hole on the ground of one-off plastic cups, the edge of the cup must be even. Then put the gold-silver thread through the hole, choose a bigger cup than the bobbin.
关于金银线车花的改善方法
The way of improving embroidery of gold-silver thread
www.chinaemblem.com

## Slide 2
第一个小旋钮40%张力
Tension for the first knob set at 40%
大旋钮40%张力
Tension for the big knob set 40%
第二个小旋钮20%张力
Tension for the second knob set at 20 %
第一和第二旋钮尽量放松（逆时针旋），保持基本与螺丝持平的状态，如图所示！
Set the first and the second knobs loose (counter-clockwise direction )as much as possible and keep the knobs to be horizontal as the screw.
see the picture
如果有白色底线被拉出布面,则调小(逆时针旋)面线张力。
If the white bobbin thread was pulled out to the face of the fabric, then adjust the tension of the face thread in a counter-clockwise direction.0
如果有面线松,则调大(顺时针旋)面线张力。
Adjust the tension of the face thread in a clockwise direction if the face thread becomes loose.
关于金银线车花的改善方法
The way of improving embroidery of gold-silver thread
www.chinaemblem.com

## Slide 3
底线要非常顺畅的能拉出来，拉出底线时，线芯要如图所示方向转动
pull out the underlay smoothly and the core of shuttle must turn around as the pictute.
底线按如图所示方向装入梭壳
Put the underlay into the shuttle as the picture
然后通过弹簧片再绕过扣线弹簧
go through the spring piece and then go through the hook.
底线如果太紧，则按图所示方向调节螺丝。
adjust the screw as the pictue if the the underlay is too tight.
关于金银线车花的改善方法
The way of improving embroidery of gold-silver thread
www.chinaemblem.com
Notes: <number>
<number>

## Slide 4
拿着线端,轻轻把梭芯壳上下摇动时, 线由于梭芯的自重能自然拉出来的状态为适当的张力
It is proper thread tension : to hand-lift the core of the shuttle and shake it from top and bottom, and the bobbin thread can be pull out smoothly
将线芯装入底梭并放入底线张力器,用螺刀调节弹簧片松紧,红色针落在红色范围内(20gf—30gf), place the core to the shuttle together with the gauge of the thread tension, adjusting the elasticity of the spring with screwdriver, setting the red pointer at 20gf – 30gf.
关于金银线车花的改善方法
The way of improving embroidery of gold-silver thread
www.chinaemblem.com